## Slide 1
SportPose
Markerless 3D Human Motion Capture via Stereo Vision
An end-to-end technical walkthrough: camera capture -> synchronization -> calibration -> triangulation -> 3D kinematics
Stereo capture · OpenCV calibration · MediaPipe pose · Metric triangulation
Notes: Open by scoping honestly: the pose model is off-the-shelf MediaPipe; our contribution is the classical stereo pipeline (calibration, synchronization, triangulation, leveling) and the full-stack app. We reconstruct TRUE metric 3D, not a monocular depth guess.

## Slide 2
EXECUTIVE SUMMARY
What SportPose is
The system in one paragraph
Two cameras record an athlete from two angles (a stereo pair).
A pre-trained pose model finds 2D body joints in each view.
Classical stereo geometry - calibration + triangulation - lifts the paired 2D joints into true 3D positions (millimetres).
3D joint angles are computed per frame and shown in a synchronized web UI: overlay video + rotatable 3D skeleton + angle graphs.
Scope of the ML: pose estimation = MediaPipe (inference only). Our engineering = the stereo reconstruction pipeline + application.
2 cams
Stereo pair -> metric depth via triangulation
18 pts
Custom skeleton (from MediaPipe's 33 landmarks)
12
Joint angles tracked per frame, in 3D
3D mm
Real-world units, not relative monocular depth
SportPose · 3D Stereo Motion Capture
1
Notes: Lead with the framing sentence in the bottom bullet. If they think you trained a network, that gets dismantled fast - own the real scope; the stereo geometry IS the substance.

## Slide 3
MOTIVATION
Why markerless 3D?
The problem
Marker-based mocap (Vicon, OptiTrack) is accurate but costly, lab-bound, needs suits + many cameras.
Single-camera 2D analysis can't measure true 3D joint angles - depth is lost.
Coaches want quantitative kinematics from ordinary hardware.
Our approach
Two consumer cameras form a calibrated stereo rig.
Markerless: pose model finds joints - no suit.
Triangulation recovers metric 3D from the two views.
Delivered as a web app: upload/record -> analyze -> visualize.
Why it's hard
Two cameras must be synchronized in time.
A wide baseline must be accurately calibrated.
2D detection noise propagates into 3D.
Left/right joint correspondence must be correct.
SportPose · 3D Stereo Motion Capture
2
Notes: Frame the value (cheap, markerless, 3D) and immediately signal you understand the hard parts - sync, calibration, noise, correspondence. This pre-empts his first questions.

## Slide 4
PART 1
System & Setup
Architecture, technology stack, camera rig, capture & synchronization

## Slide 5
ARCHITECTURE
System architecture
Client - React 19 SPA
Vite - TypeScript - Tailwind
React Router - TanStack Query
ECharts - Canvas 3D viewer
API - FastAPI (Uvicorn)
Routers: users - upload - pose
camera - obs - ping
JWT auth (HttpOnly cookie) - CORS
HTTPS - cookie
Vision Engine (Python)
MediaPipe Pose Landmarker
OpenCV - NumPy
Calibration - Triangulation
MongoDB
Collections: users, videos,
pose_analysis (keypoints,
3D frames, angles, status)
MinIO (S3 object store)
Raw + processed videos.
Accessed by clients via
1-hour presigned URLs.
Keyword recap: SPA - REST - JWT/HttpOnly cookie - object storage - presigned URL - document DB - synchronous processing
SportPose · 3D Stereo Motion Capture
3
Notes: The browser never touches MinIO credentials - it gets short-lived presigned URLs. Processing currently runs synchronously inside the FastAPI request (flag this; it's a scalability limit you'll revisit).

## Slide 6
TECHNOLOGY
Technology stack & keywords
Frontend
React 19 + TypeScript, Vite
Tailwind CSS v4, Framer Motion
TanStack Query (server cache)
ECharts + HTML Canvas (3D)
Backend
FastAPI + Uvicorn (ASGI)
Pydantic models, CORS
PyMongo, python-dotenv
JWT (PyJWT) + bcrypt auth
Computer vision
MediaPipe Tasks - Pose Landmarker
OpenCV (calibrate, triangulate)
NumPy linear algebra
obsws / DroidCam capture
Storage
MongoDB - metadata & results
MinIO - S3-compatible objects
Presigned URLs for playback
Temp files during processing
Capture
USB webcams (DirectShow)
Phone IP-cams over WiFi
MJPEG live preview stream
cv2.VideoWriter (avc1/mp4v)
Calibration math
Checkerboard detection
Intrinsics + distortion model
Stereo extrinsics (R, T)
DLT triangulation, plane fit
SportPose · 3D Stereo Motion Capture
4
Notes: Be ready to justify each choice. MediaPipe = fast, robust, per-point confidence, tiny footprint. FastAPI = async, typed. MinIO = self-hosted S3 so we never ship blobs through the DB.

## Slide 7
PIPELINE
End-to-end pipeline at a glance
0
Calibrate
One-time: intrinsics, distortion, R, T from a checkerboard
1
Capture
Two synchronized views -> live preview
2
Record + store
Side-by-side MP4 -> MinIO + MongoDB
3
Trigger + route
Stereo vs 2D path decided by metadata
4
2D pose
MediaPipe on each view -> 18 keypoints
5
Triangulate
Paired 2D -> metric 3D (mm), left-cam frame
6
3D angles
12 joint angles per frame + floor leveling
7
Persist + show
Results stored -> synchronized web visualization
SportPose · 3D Stereo Motion Capture
5
Notes: This is the spine of the talk. Everything after is a zoom-in on one of these stages. If asked to walk through it, follow these eight rows in order.

## Slide 8
CAMERA SETUP
Physical camera rig (top-down)
305 cm
381 cm
Cam L
Cam R
Capture
volume
(athlete)
baseline
~ 3.6 m
Rig parameters
Two cameras fixed on the same wall, ~3.6 m apart (wide baseline).
Mounted ~2 m high, both tilted down toward the capture volume.
Convergent (verged) setup - optical axes meet in the shared volume, not parallel.
Athlete performs inside the overlapping field of view (the red box) - the only region both cameras see well.
Trade-off: a wide baseline gives better depth precision but makes calibration & correspondence harder.
Consequence: the 3D is reconstructed in the LEFT camera's coordinate frame; a floor-leveling step re-orients it upright.
SportPose · 3D Stereo Motion Capture
6
Notes: This mirrors your real room (305x381 cm). Key terms: baseline, convergent/verged rig, overlapping field of view, capture volume. Wide baseline = the reason calibration is hard and why depth precision is good.

## Slide 9
CAMERA SETUP
Capture modes & signal path
USB mode
Two USB webcams via OpenCV + DirectShow
MJPG @ 1280x720, buffer size 1
Fails if a cam is held by OBS/Zoom
Config: CAMERA_LEFT/RIGHT_INDEX
WEB (phone) mode
Two phones as IP cameras (DroidCam)
Each on its own WiFi stream
Avoids shared USB-bus contention
Config: PHONE_1_IP / PHONE_2_IP
Also available
OBS Studio start/stop via WebSocket
Nikon DSLR (offline) for clean 2D + validation reference
Any uploaded MP4/MOV/AVI -> 2D path
Signal path
Cameras
Grab thread
(L then R)
Compose
side-by-side
MJPEG
live preview
VideoWriter
MP4
Upload ->
MinIO
SportPose · 3D Stereo Motion Capture
7
Notes: Two live modes: USB and phone-IP. Phones avoid USB-bus contention - a real practical reason. The DSLR can't live-stream/sync, so it's for clean single-camera 2D and as an accuracy reference.

## Slide 10
STAGE 1 · CAPTURE
Capture & synchronization
How a synchronized pair is formed
One background thread reads both cameras sequentially: read(L) then read(R).
Buffer size = 1 to keep only the freshest frame (low latency).
Last-good frame from each side is cached; newest (L, R, timestamp) is published.
Live preview served as an MJPEG multipart stream.
Calibration capture uses the tighter grab()+grab() -> retrieve() pattern.
Timeline (one capture cycle)
read L
read R
dt offset (a few ms)
! Software sync - the key limitation
Not hardware-genlocked. The L/R frames are a few ms-tens of ms apart, and the offset varies under load.
Triangulation error ~ motion_speed x dt. Worst on fast limbs; negligible on slow/still motion.
Example: 20 ms offset, wrist at 2 m/s -> ~4 cm apparent displacement between views.
Recording uses read()/read() - looser than the grab()/retrieve() used in calibration (an easy internal fix).
Proper fixes: hardware genlock / external trigger, or timestamp each stream and interpolate to a common clock.
SportPose · 3D Stereo Motion Capture
8
Notes: THIS is the question he opens with. Say not hardware-synced first, then quantify the error and give the fix. Never let him extract this - volunteer it.

## Slide 11
STAGE 2 · RECORD
Recording & storage
Side-by-side composite frame (one file)
LEFT view
RIGHT view
cv2.hconcat -> one MP4
Frame pacing
Writer paced to the wall clock: expected = elapsed x fps.
Duplicates the latest frame to catch up so duration is correct.
Caveat: fps is nominal - under-delivery -> repeated frames (zero-velocity artifacts).
What gets stored, and where
MinIO (object store)
Raw recording, then the processed overlay video.
Unique UUID object names; retrieved via 1-hour presigned URLs.
MongoDB - videos document
user_id, bucket, object_name, filename, size, uploaded_at.
Stereo tags: source='stereo_camera', layout='side_by_side', fps, frames.
These tags later route the clip to the 3D pipeline.
Keywords: composite frame - wall-clock pacing - object storage - presigned URL - metadata tagging
SportPose · 3D Stereo Motion Capture
9
Notes: The layout/source tags written here are what Stage 3 reads to choose stereo-vs-2D. Mention the frame-duplication caveat before he finds it.

## Slide 12
PART 2
Calibration
Teaching the system the geometry of the two cameras

## Slide 13
CALIBRATION · CONCEPT
What calibration recovers
Intrinsics (K)
per camera
Focal length + optical/principal point.
How this lens maps the world onto pixels.
Distortion (D)
per camera
Radial + tangential lens bending.
Mathematically undone before triangulating.
Extrinsics (R, T)
between cameras
Rotation R and translation T of the right camera relative to the left.
T is in millimetres (set by square size).
Why it matters
the payoff
Only with K, D, R, T can two 2D points be intersected into one correct 3D point.
Errors here tilt/skew the whole skeleton.
SportPose · 3D Stereo Motion Capture
10
Notes: Define these four crisply - a definitions question is a trap to check you understand your own system. Intrinsics vs extrinsics is the classic one.

## Slide 14
CALIBRATION · PROCESS
Calibration procedure (offline, one-time)
1
Print target
9x6 inner-corner checkerboard, 40 mm squares. Known geometry sets the metric scale.
2
Detect corners
findChessboardCorners + sub-pixel cornerSubPix, in BOTH views simultaneously.
3
Capture ~20 pairs
SPACE stores a pair only if the board is found in both views; vary pose/tilt/distance.
4
Per-camera solve
cv2.calibrateCamera -> K, D and a left/right RMS for each camera.
5
Stereo solve
cv2.stereoCalibrateExtended (FIX_INTRINSIC) -> R, T + per-pair errors.
6
Reject + refit
Drop outlier pairs, recalibrate on survivors (next slide).
7
Save
calibration.npz: K1,D1,K2,D2,R,T, sizes, RMS, square size (+ floor R_level).
SportPose · 3D Stereo Motion Capture
11
Notes: Emphasize step 3's gate (board must be in BOTH views) and that the square size is what makes everything metric. Quality is judged by reprojection RMS.

## Slide 15
CALIBRATION · QUALITY CONTROL
How bad image pairs are removed
1
Gate 1 - at capture (prevention)
A pair is stored only if the checkerboard is detected in BOTH views on a fresh synced grab.
If the board isn't cleanly visible in both -> the pair is never added.
2
Gate 2 - at calibration (outliers)
stereoCalibrateExtended returns a per-pair reprojection error.
threshold = max(1.0 px, 1.5 x median error).
Pairs above threshold are dropped; recalibrate on the rest - only if >= 8 good pairs remain.
Reprojection error (the metric)
Project the reconstructed 3D board points back into the image.
Measure pixel distance to the actually-detected corners.
RMS of those distances summarizes the fit - lower is better; target < 1.0 px.
Honest caveat
The median x 1.5 rule is a practical filter, not a formal robust estimator (MAD/z-score would be stronger).
Currently evaluated on the same pairs used to fit - no held-out set yet.
SportPose · 3D Stereo Motion Capture
12
Notes: This is the exact question your client already asked. Know both gates and the median x 1.5 rule. Volunteering the two caveats reads as maturity, not weakness.

## Slide 16
CALIBRATION · REALITY CHECK
Quality metrics & the wide-baseline challenge
< 1.0 px
Target stereo RMS
~4.2 px
Current stereo RMS (to fix)
3.6 m
Real baseline (measured)
+-15%
Baseline sanity-check band
Why our RMS is high right now
3.6 m baseline calibrated with a small 40 cm board -> few pixels per corner.
Steep convergence angle -> the board is foreshortened in at least one view.
Per-camera RMS was fine (1.6 / 0.27 px) but stereo RMS was ~4.2 -> a synchronization / correspondence issue, not a lens issue.
A per-pair median of 5.6 px meant most pairs were bad, not just outliers.
Fixes in progress
Larger / higher-resolution calibration target.
Hold the board perfectly still; keep both cameras rigid.
Added baseline sanity check: |T| vs measured 3.6 m, warns if >15% off.
Added floor-leveling to fix orientation independently.
Realistic goal for this rig: ~1-1.5 px.
SportPose · 3D Stereo Motion Capture
13
Notes: Don't hide the 4.2 px. Explain WHY (wide baseline + small board + sync), what it tells you (per-camera good, stereo bad = sync), and the concrete fixes. This is exactly the diagnostic reasoning a senior engineer wants to see.

## Slide 17
CALIBRATION · LEVELING
Floor leveling - standing the skeleton upright
Camera tilted down ->
skeleton appears tilted
R_level
Leveled &
upright
How it works
Lay the checkerboard flat on the floor; capture it in both cameras (press 'f').
Triangulate its corners -> fit a plane -> the plane normal is 'up'.
Compute a rotation R_level that maps that normal to the vertical axis.
Store R_level in calibration.npz; apply it to every 3D frame at analysis time.
Joint ANGLES are rotation-invariant, so leveling changes only the display orientation - never the measured numbers.
SportPose · 3D Stereo Motion Capture
14
Notes: Two separate causes of tilt: (1) calibration error in R, fixed by better calibration; (2) output is in the tilted left-camera frame - fixed by R_level. Stress that leveling is cosmetic: angles don't change.

## Slide 18
PART 3
The 3D Pipeline
From pixels to metric 3D joint angles, then to the screen

## Slide 19
STAGE 4 · 2D POSE
2D pose estimation (per view)
MediaPipe Pose Landmarker
Tasks API, VIDEO running mode, model file pose_landmarker.task.
Per frame: BGR->RGB -> detect_for_video with a 30 fps-locked timestamp.
Returns 33 landmarks; we remap to a custom 18-point skeleton and synthesize a NECK = midpoint of the two shoulders.
Keypoints stored NORMALIZED [x, y, presence] in 0-1.
For stereo, this runs twice - left half and right half - with temporal healing OFF.
We do NOT use MediaPipe's z (monocular, relative). Real depth comes from triangulation.
33 landmarks -> 18-point skeleton
MediaPipe
33 landmarks
Remap + synth neck
-> 18 keypoints
● left ● right ● centre
SportPose · 3D Stereo Motion Capture
15
Notes: Strong point: we ignore MediaPipe's z because it's a relative monocular guess. Weakness to flag next slide: presence vs visibility, and healing is off on the 3D path.

## Slide 20
REPRESENTATION
The 18-point skeleton & connections
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
Keypoint index map
0 Nose
1 Neck (synthesized)
2 L shoulder 3 R shoulder
4 L elbow 5 R elbow
6 L wrist 7 R wrist
8 L index 9 R index
10 L hip 11 R hip
12 L knee 13 R knee
14 L ankle 15 R ankle
16 L foot 17 R foot
Bones: 18 connections (arms,
legs, spine, shoulder & pelvis girdles)
Angles computed: knees, hips, elbows, wrists, shoulders, ankles (left & right = 12).
SportPose · 3D Stereo Motion Capture
16
Notes: The neck is not a MediaPipe landmark - we build it from the shoulder midpoint so the skeleton has a clean spine for angle definitions.

## Slide 21
STAGE 5 · TRIANGULATION
Paired 2D -> metric 3D
Left cam
Right cam
P = (X, Y, Z) mm
baseline R, T
Two rays, one intersection -> depth
Method (standard, robust)
Convert normalized keypoints -> pixels using each view's stored size.
cv2.undistortPoints - removes distortion + intrinsics -> normalized camera rays.
Projection matrices: P1 = [ I | 0 ], P2 = [ R | T ].
cv2.triangulatePoints (linear DLT) -> homogeneous -> divide -> 3D in the LEFT-camera frame, in mm.
A joint below 0.5 confidence in EITHER view -> NaN (gap), never a wrong point.
Limits: linear DLT (algebraic error), no per-joint outlier rejection, no bundle adjustment, no epipolar correspondence check.
SportPose · 3D Stereo Motion Capture
17
Notes: Name the method precisely (DLT via SVD, algebraic error) and its limits (no outlier rejection, no bundle adjustment, no epipolar gating). The epipolar/correspondence gap is the second question he'll dig at.

## Slide 22
STAGE 6 · KINEMATICS
3D joint angles
Computation
For a joint at B with neighbours A and C: form vectors A-B and C-B.
Angle = arccos of their normalized dot product - a true 3D angle.
12 angles per frame: knees, hips, elbows, wrists, shoulders, ankles (L & R).
A missing (NaN) endpoint -> that angle is simply skipped for the frame.
theta = arccos( (A-B).(C-B) / |A-B| |C-B| )
in 3D - no camera-facing heuristics needed
Why this output is robust
Angles are INVARIANT to scale - a wrong square size mis-sizes positions but not angles.
Angles are INVARIANT to global rotation - camera tilt / leveling doesn't change them.
So many calibration errors hurt the 3D picture more than the numbers we actually report.
The 2D path additionally uses a facing-direction normalization + anatomical convention; the 3D path needs none of that.
SportPose · 3D Stereo Motion Capture
18
Notes: This is your single best defensive slide. The reported deliverable (angles) is invariant to scale and global rotation - exactly the invariances that neutralize the calibration weaknesses he'll probe.

## Slide 23
STAGE 7 · PERSISTENCE
Storing the results
On the process-video request
Download clip from MinIO to a temp file.
Route: layout=='side_by_side' (or source=='stereo_camera') AND calibration.npz exists -> 3D path; else 2D.
Run pose + triangulation; render the left-view overlay video.
Re-upload the overlay to MinIO as processed_object_name.
Runs synchronously inside the HTTP request (a scalability limit).
pose_analysis document
video_id, user_id, status, created_at.
result.frames - per-frame 2D keypoints + 2D angles (drives the graph).
result.frames_3d - triangulated 3D points + true 3D angles (drives the 3D viewer).
result.mode = 'stereo_3d', units = 'mm', fps, total_frames.
One document per video; upsert on re-processing.
SportPose · 3D Stereo Motion Capture
19
Notes: Note the dual payload: 2D frames keep the chart working; frames_3d powers the 3D viewer. Flag synchronous processing as the production gap (needs a job queue).

## Slide 24
STAGE 8 · VISUALIZATION
Frontend & time synchronization
Analysis page - 3 synced panels
Overlay video
(2D skeleton)
Rotatable 3D
skeleton viewer
Joint-angle graph (ECharts) - angle vs time
Event-driven time sync
On each animation frame the video dispatches a 'sync-time' window event with currentTime.
The graph moves a vertical marker line to that time (throttled ~20 fps).
The 3D viewer jumps to frame = floor(time x fps).
'analysis-complete' event invalidates the TanStack Query cache to refetch results.
Keywords: SPA - custom DOM events - requestAnimationFrame - throttling - query invalidation - presigned playback URL
SportPose · 3D Stereo Motion Capture
20
Notes: The three panels stay locked to the video clock via a lightweight custom-event bus - no heavy state library needed. Playback uses a short-lived presigned MinIO URL.

## Slide 25
VISUALIZATION
The 3D skeleton viewer
Rendering
Pure HTML Canvas - a hand-written 3D->2D projection (no Three.js).
Manual yaw / pitch / zoom via mouse drag + wheel.
Auto-centers and scales to the reconstructed point cloud.
Draws bones (left/right/centre coloured), joints, and a floor grid.
Live HUD lists the current frame's 3D joint angles.
Reads frames_3d for the selected video; rotates with R_level so the athlete stands upright.
SportPose · 3D Stereo Motion Capture
21
Notes: Deliberately lightweight (canvas, not a 3D engine) - fewer dependencies, full control over the projection and the biometrics HUD.

## Slide 26
RECAP
End-to-end data flow
Capture
Side-by-side
MP4
MinIO +
MongoDB
Split L / R
MediaPipe
2D x 2
Triangulate
-> 3D mm
Angles +
R_level
Store
pose_analysis
Synced
web UI
Offline, once
Stereo calibration -> calibration.npz (K, D, R, T).
Floor leveling -> R_level.
Reused by every subsequent recording.
Per clip, on demand
Triggered by the 'Extract Kinematics' button.
Everything from split -> 3D -> store runs server-side.
Results cached; UI refetches on completion.
SportPose · 3D Stereo Motion Capture
22
Notes: Use this to answer walk me through it end to end in 30 seconds. Calibration is the one-time offline branch; everything else runs per clip.

## Slide 27
CROSS-CUTTING
Authentication & security
Authentication
Login verifies bcrypt password hash.
Issues a signed JWT (HS256).
Stored in an HttpOnly cookie - not readable by JS (XSS-safer).
/me validates the cookie on load.
Authorization
Role claim in the token (admin / user).
FastAPI dependencies: get_current_user, require_admin.
Users see only their own videos; admin can access all.
Data access
MinIO never exposed to the browser.
Short-lived (1-hour) presigned URLs for playback.
CORS locked to the known frontend origins.
Ownership checked on every video route.
SportPose · 3D Stereo Motion Capture
23
Notes: HttpOnly cookie = the token is invisible to JavaScript, reducing XSS token theft. Presigned URLs mean the browser streams video without ever seeing storage credentials.

## Slide 28
PART 4
Engineering Review
Known limitations, hard questions, and the roadmap

## Slide 29
MATURITY
Known limitations (we volunteer these)
Synchronization
Software-level sequential reads; no genlock. Recording sync looser than calibration.
Correspondence
No epipolar check before triangulation - a MediaPipe L/R label flip would mis-pair joints.
Triangulation
Linear DLT, no per-joint outlier rejection, no bundle adjustment.
Temporal filtering
3D path runs raw (healing off) - no Kalman / One-Euro smoothing.
Calibration
~4.2 px RMS now; fit-set evaluation; median x 1.5 outlier rule is heuristic.
Frame rate
fps hardcoded to 30; nominal fps via frame duplication.
Confidence
Uses 'presence', not 'visibility'; no cross-view occlusion fallback.
Scope
Single person; synchronous processing; accuracy not yet quantified.
SportPose · 3D Stereo Motion Capture
24
Notes: Say these before he digs them out - it flips every one from a gotcha into evidence of self-awareness. Have the fix ready for each (next slides).

## Slide 30
ANTICIPATED QUESTIONS I
The questions he WILL ask (1/2)
Q How are the cameras synchronized? Prove it.
A Not hardware-synced - sequential reads, few ms-tens of ms, variable. Error ~ speed x dt, worst on fast limbs. Fix: genlock or timestamp + interpolate.
Q How do you know left-joint-j = right-joint-j?
A We pair by index and trust MediaPipe labeling. No epipolar check yet - a facing-away label flip would mis-pair. Fix: epipolar / essential-matrix gating.
Q What triangulation, and what does it optimize?
A Linear DLT (SVD), minimizes algebraic error, no outlier rejection. Improve with optimal triangulation, RANSAC gating, bundle adjustment.
Q What's your confidence signal? Occlusion?
A MediaPipe 'presence' > 0.5 per view; weak joint -> NaN. 'visibility' may suit occlusion better; no cross-view fallback.
SportPose · 3D Stereo Motion Capture
25
Notes: Rehearse these four out loud. Lead each answer with the honest admission, then the quantification, then the fix.

## Slide 31
ANTICIPATED QUESTIONS II
The questions he WILL ask (2/2)
Q MediaPipe already gives z - why triangulate?
A Its z is monocular, relative, hip-anchored - not metric. Stereo gives TRUE mm depth from real geometry.
Q Units and scale - what if scale is wrong?
A 3D in left-cam frame, mm, scale from square size. But our OUTPUT is angles - invariant to scale and global rotation.
Q Latency and scale to many users?
A process-video is synchronous in the request. Production needs an async job queue + GPU; frame duplication makes fps nominal.
Q What is your accuracy, in degrees?
A Not yet quantified. Plan: DSLR side-on 2D reference + goniometer on static poses -> report mean absolute error.
SportPose · 3D Stereo Motion Capture
26
Notes: The accuracy in degrees answer must NOT invent a number. Say you haven't measured it and give the exact validation method. That honesty scores higher than a fake figure.

## Slide 32
ROADMAP
Future work
Accuracy
Hardware genlock / trigger sync
Epipolar correspondence gating
Optimal triangulation + RANSAC
Bundle adjustment (n-camera)
Robustness
Kalman / One-Euro temporal filter
Cross-view occlusion recovery
Read true fps (remove 30 hardcode)
Larger calibration target + held-out RMS
Product
Async job queue + progress
GPU inference
Multi-person + view association
Quantified accuracy report
SportPose · 3D Stereo Motion Capture
27
Notes: Each future-work item maps 1:1 to a limitation - show that you have a concrete plan, not just a list of problems.

## Slide 33
VALIDATION PLAN
Proving accuracy (what we'll measure)
Reference: DSLR 2D
Nikon D3400 on tripod, side-on.
Perpendicular to the plane of motion.
Clean planar joint-angle reference.
Record at 30 fps to match pipeline.
Reference: goniometer
Physically measure static joint angles.
Compare to the system's 3D angle for the same pose.
Simple, cheap ground truth.
Metric
Mean absolute error (degrees).
Per joint + overall.
Report across poses and speeds.
Track improvement vs baseline.
Honesty rule: until measured, we state 'not yet quantified' and show the method - never a fabricated number.
SportPose · 3D Stereo Motion Capture
28
Notes: Having a concrete validation protocol ready is often worth more than a number - it shows you know how to prove the system, not just build it.

## Slide 34
REFERENCE
Key terms glossary
Intrinsics / Extrinsics - Internal optics (focal length, principal point) / rotation+translation between the two cameras.
Epipolar geometry - A point in one view lies on a line in the other (fundamental/essential matrix) - used to validate matches.
Triangulation (DLT) - Intersecting two back-projected rays to recover a 3D point; Direct Linear Transform solves it linearly.
Reprojection error / RMS - Pixel gap between detected and reprojected points; RMS summarizes calibration accuracy (< 1 px target).
Bundle adjustment - Jointly optimizing 3D points + camera params to minimize total reprojection error (gold standard).
Baseline - Distance between the two camera centres (|T|); wider = better depth precision, harder correspondence.
Genlock - Hardware synchronization of cameras to a common trigger/clock.
Rolling vs global shutter - Rows exposed sequentially vs all at once; rolling shutter skews fast motion.
Presence vs visibility - MediaPipe: landmark is in-image vs landmark is visible (not occluded).
Kalman / One-Euro filter - Temporal filters that smooth jittery keypoints while tracking real motion.
SportPose · 3D Stereo Motion Capture
29
Notes: A definitions question is a competence test. If asked any of these, answer in one clean sentence - don't ramble.

## Slide 35
Thank you
Questions & discussion
Remember: state the mechanism, volunteer the limitation, give the fix. Honesty > a confident wrong answer.
Notes: Close calm. Invite the hard questions - you've prepared for them. If cornered: I haven't measured/built that - here's why it matters and how I'd approach it.